# Supplemental Information for

"Wave propagation through disordered media without backscattering and intensity variations"

Konstantinos G. Makris1, Andre Brandstötter2, Philipp Ambichl2, Ziad H. Musslimani3, and Stefan Rotter2

1Crete Center for Quantum Complexity and Nanotechnology, Department of Physics, University of Crete, Heraklion 71003, Greece

2Institute for Theoretical Physics, Vienna University of Technology, Vienna 1040, Austria

3Department of Mathematics, Florida State University, Tallahassee, Florida 32306, USA

Email: KGM, makris@physics.uoc.gr; AB, andre.brandstoetter@tuwien.ac.at; 
 PA, philipp.ambichl@tuwien.ac.at; ZHM, muslimani@math.fsu.edu; SR, stefan.rotter@tuwien.ac.at 
Correspondence: KGM, Email: makris@physics.uoc.gr, Phone: 30-2810-394227

WKB analysis. Expanding the function  in powers of a small parameter , , and inserting it into the Helmholtz Eq. (1) to leading order, we can show that in the limit of ,  scales with . Setting  and collecting terms with the same power of , we can write down the two dominant terms, namely , and . To each of these terms a corresponding equation is found:

(0.1)

. 				(0.2)

The exactness requirement of our ansatz necessitates that all terms  are zero and the demand for constant intensity of  calls for a real-valued . Both conditions can be fulfilled by choosing  such that the term  moves from Eq. (0.1) to Eq. (0.2), leading to  and

. As a result  and all higher terms are constant as well.

Setting , we finally obtain the non-Hermitian dielectric function (relative permittivity), as shown in Eq. (2).

Iteration technique for determination of the gain-loss profile given the  distribution. Given the function , the dielectric distribution  and the corresponding refractive index distribution can be directly determined and vice versa. The same is, however, not true if, as a starting point, the real part of the refractive index  is known instead (typical situation in many realistic cases). The reason is that by adding an imaginary part of the refractive index  (e.g., by pumping), one not only changes  but also . In other words, by adding gain and loss to a material, the real part of the dielectric function changes as well. In order to overcome such a problem, we employ an iterative technique, that is based on the following expressions between  and the complex index of refraction:  and . To identify  and  required for CI-states (that correspond to a specific and given  distribution), we applied an iterative numerical scheme that allows to determine these unknown distributions, by starting with a reasonable guess function for . In particular, at the  step of iteration the equations read:

(0.3)

,				 (0.4)

where  is the given wavenumber of the incident plane wave. We explicitly checked that the method converges and leads to the desired results.

Effects of gain saturation. We prove here that the constant-intensity state can be a scattering eigenstate mode under perfect transmission boundary conditions in a medium with gain saturation1.  The corresponding nonlinear Helmholtz equation is:

, 		(0.5)

where  describes the material loss in the cavity, the pump, and  the saturation coefficient. We are looking for constant-intensity states of the form

,				 (0.6)

where the amplitude  of the solution plays an important role now. The nonlinear Eq. (0.5) can be written in the form of Eq. (1) with an effective complex permittivity , defined as follows:

. 		(0.7)

By substitution of Eq. (0.7) into Eq. (0.5) we obtain the following equations:

, 			(0.8)

. 			(0.9)

Given the auxiliary function  the real part of the permittivity can be easily determined by the above Eq. (0.8). Regarding the imaginary part of the permittivity, and, the pump profile , these can be determined as follows:

(0.10)

(0.11)

## REFERENCES

1	Premaratne M, Agrawal GP. Light Propagation in Gain Media: Optical Amplifiers. Cambridge University Press: Cambridge, 2011.